Leveling Sensor eLiSe

- General Information

| Geometrical Dimensions | without triangular base plate |
| --- | --- |
| Outer Diameter Bubble Level | 15.0 mm |
| Height of the Bubbel Level | 15.5 mm |
| Length of the Flexband | 100 mm |
| Working Temperature | 0°C … 40°C |
| Storage Temperature | -20°C … 60°C |
| Supply Voltage | 2.7 V … 5.5 V, typ. 5.0 V |
| LED Current | 3 mA … 20 mA, typ. 3 mA … 5 mA |
| PIN Assignment |  |

- Resolution, Accuracy and Reproducibility

Resolution, accuracy and reproducibility are influenced by both the sensor itself and by the data analysis electronics. Within a tilting range of 3’ (angular minutes) around the “leveling point” (tilting in both directions is equal to zero) the sensor yields.

| Tilting Range | typ. 3’, max. 15’ |
| --- | --- |
| Resolution | 8” |
| Accuracy | 30” |
| Reproducibility | 15” |

Comments:

- At the levelling point both accuracy and repeatability are equal and amount to 15”.

- About response time: After stop of a tilting movement the sensor signal settles to the upper stated accuracy/repeatability within 8 sec. After 1 sec the errors are about twice higher.

- The sensor signal really is affected by vibration. Vibration causes least errors at the levelling point.

- Interface Definition of the Evaluation Kit

Serial Interface:

- 19200 Baud

- 8 Bit

- 1 Stopbit

- No Parity

Protocol:

- Format data communication: ASCII-Format.

- Firmware version:	„$?“ + <CR> 	Answer: VX.X <LF>

- Data: „1“ ->	Answer:  AAAA, BBBB, CCCC, DDDD, 0, 0, <LF>

- Value range: 1…1024

D1 … AAAA

D2 … BBBB

D3 …CCCC

D4 … DDDD

- Set LED current: „:IXXX“+ <CR>	XXX: 050…255 (RESET value: 110)